## Slide 1: Open-Source EDA
-Rishikesh K

## Slide 2: Index
Yosys Installation
OpenSTA Installation
OpenROAD Installation
Logic Synthesis using Yosys
Timing & Power Analysis Using OpenSTA
Physical Design using OpenROAD

## Slide 3: Yosys Installation
• Install all prerequisites for building yosys:
$ sudo apt−get install build−essential clang bison flex \
libreadline −dev gawk tcl−dev libffi −dev git \
graphviz xdot pkg−config python3 libboost−system−dev \
libboost−python−dev libboost−filesystem−dev zlib1g−dev
• Clone the GitHub repository
$ git clone https://github .com/YosysHQ/yosys . Git
$cd yosys
$ git submodule update --init
$make
$sudo make install
To Invoke the tool type “yosys”

## Slide 4: OpenSTA Installation
Required Dependencies
cmake 3.10.2 ,clang 9.1.0 ,gcc 3.3.2 , tcl 8.4 ,swig 1.3.28
bison 1.35, flex 2.5.4
Clone the OpenSTA repository by executing the following command:
$git clone https://github.com/The-OpenROAD-Project/OpenSTA.git
$cd OpenSTA
$mkdir build && cd build
$cmake ..
$make
$sudo make install
Cmd to Invoke “sta”

## Slide 5: OpenROAD Installation
Clone the OpenSTA repository by executing the following command
$ git clone --recursive https://github.com/The-OpenROAD-Project/OpenROAD.git
$ cd OpenROAD
$ sudo ./etc/DependencyInstaller.sh
$ mkdir build && cd build
$ cmake ..
$ make
$ sudo make install
To Invoke “openroad”, gui mode “openroad –gui”

## Slide 6: Logic synthesis Using Yosys
Synthesis TCL Script
# Read modules from Verilog file
read_verilog top.v
# Elaborate design hierarchy
hierarchy −check −top top
# Translate processes to netlists
proc
# Mapping to the internal cell library
techmap
# Mapping flip−flops to liberty file
# for e.g., always block

## Slide 7
dfflibmap −liberty <liberty_file.lib>
# Mapping logic to NangateOpenCellLibrary
# for e.g., assign block
abc −liberty <liberty_file> –constr <constraints.sdc>
# Remove unused cells and wires
clean
# Write the current design to a Verilog file
write_verilog −noattr netlist.v

## Slide 8
Constrains(.SDC File)
create_clock -name CLK -period 10 –waveform {0.00 5.00} [get_ports clk]
#Defines a clock named "CLK" with a period of 10ns
set_input_delay 5 -clock CLK [get_ports rst]
#Sets an input delay of 5 ns for the input port “rst" with respect to the clock "CLK.“
set_output_delay 5 -clock CLK [get_ports count]
# Sets an output delay of 5 ns for the output port “count" with respect to the clock "CLK."
set_timing_derate –late 0.9
set_timing_derate –early 1
#On-Chip Variation

## Slide 9
Execution
Type ‘yosys’ in the terminal
Either use command line method
Or save all commands in a tcl script and use
yosys> script script.tcl
4. To view the area consumed by the design use “stat -liberty<.lib _file>
5. To view the Schematic of the Circuit use “show” command
References
Installation steps for Yosys Open SYnthesis Suite. [Online]. Available: https: //github.com/YosysHQ/yosys
Yosys: Example Usage. [Online]. Available: https://yosyshq.net/yosys/ [4] Documentation for Yosys Open SYnthesis Suite commands.
Available: https://yosyshq.readthedocs.io/projects/yosys/en/manual-rewrite/cmd ref.htm

## Slide 10: Timing Analysis Using OpenSTA
Top.v
Top.sdc
Lib_file
Tcl_script
TCL Script
read_liberty <liberty_file>
read_verilog <top.v>
link_design top
read_sdc <constraints.sdc>
report_checks -path_delay max > max_reports.txt
report_checks -path_delay min > min_reports.txt
#power_Report
Set_power_activity –global –activity 0.1
Report_power > pow_report.txt

## Slide 11
Ptot =CL VDD2 α (Switching Power)+ VDDISC (short Circuit)+VDD ILEAK (Leakage)
The activity 0.1 in the command
“set_power_activity –global –activity 0.1” refers to the α
Execution
Type ‘sta’ in the terminal
Either give command by command directly in the sta terminal
Or save all commands in a tcl script and use
% source script.tcl

## Slide 12: Physical Design using OpenROAD
Type “openroad –gui” to invoke the openroad tool in gui mode
Store all required files in the working directory
Required Files
- .lib file
- Gate Level Netlist
-Timing Constraints(SDC file)
-lef file
-Tech Lef File
- .PDN file

## Slide 13: Setting Variables
Write a tcl script that source the required scripts
-Source the flow_helpers.tcl, helpers.tcl, and .var file the library used
Set the variables
-Top Module
- SDC File
-Netlist
-Core and Die Area

## Slide 14
TCL Script
source "helpers.tcl“
source "flow_helpers.tcl"
source "Nangate45/Nangate45.vars“
set design “top"
set top_module “top"
set synth_verilog “netlist.v“
set sdc_file “constraints.sdc"
set die_area {0 0 100 100}
set core_area {15 15 85 85}
source -echo "flow.tcl”

## Slide 15
Helpers and flow_helpers has the functions and procedural blocks execute PD
Var file has the other files like lef and tech used in the design, check the vars file that the library file use to synthesis the design and the library file called in the var file in same.
Set core area {0 0 100 100}
Set die area {15 15 85 85}
-1st Digit is the X co-ordinate of Lower Left Corner
-2nd Digit is the Y co-ordinate of Lower Left Corner
-3rd Digit is the X co-ordinate of Upper Right Corner
-4th Digit is the Y co-ordinate of Upper Right Corner